## Slide 1
Radiation study of FPGAs with neutron
beam for COMET Phase-I
Yu Nakazawa1, Yuki Fuji2, Eitaro Hamada2, MyeongJae Lee3, Yuta Miyazaki4, Akira Sato1, Kazuki Ueno2, Hisataka Yoshida1, Jie Zhang5
1Osaka University, Osaka, Japan; 2KEK, Tsukuba, Japan; 3IBS/KAIST, Daejeon, Korea; 4Kyushu University, Fukuoka, Japan; 5IHEP, Beijing China
Neutron fluence in COMET Phase-I
: 1.0 x 1012 neutron/cm2 (1MeVeq)
150 days measurement time
safety factor of 5~10
Front-end electronics
FPGAs are used for digital signal processing
Neutron damage
Due to the neutron-nuclear interaction, a logic in FPGA can be affected.
Neutron irradiation test
TANDEM @Kobe Univ.
  2 MeV neutron beam
  Flux: 1.9 MHz/cm2/µA @ 10 cm from the source
Evaluation Item
  Soft error rate
    CRAM SEU & URE
    BRAM SEU & MBE
  Recovery system
  TMR operation
 | FPGA | FPGA Size [mm]
RECBE | Virtex-5 (XC5VLX155T-1FFG1738C) | 35 x 35
ROESTI | Artix-7 (XC7A200T-2FBG676C) | 27 x 27
COTTTRI | Artix-7 (XC7A200T-2FFG1156C) | 35 x 35
FCT | Kintex-7 (XC7K160T-2FFG676C) | 27 x 27
RECBE
COTTRI
ROESTI
FCT
Auto-recovery system
Most of the soft errors can be repaired.
Re-downloading function is needed when an unrecoverable soft error (URE) occurs.
Result
No permanent damage
Success
  Auto-recovery system
  TMR
  Re-downloading function
Incident angular dependence
SEU rate
FPGA dependence of CRAM SEU rate was measured.
Dead time by soft errors can be suppressed by auto-recovery systems.
Frontier Detector for Frontier Physics: 14th Pisa Meeting on Advanced Detectors, La Biodola, Isola d’Elba, Italy, May 27th – June 2nd 2018